## Slide 1: OFIWG Scalable Fabrics Tutorial: Building OpenSHMEM
Charles Archer

## Slide 2: Legal Disclaimer & Optimization Notice
PGAS 2014
INFORMATION IN THIS DOCUMENT IS PROVIDED “AS IS”. NO LICENSE, EXPRESS OR IMPLIED, BY ESTOPPEL OR OTHERWISE, TO ANY INTELLECTUAL PROPERTY RIGHTS IS GRANTED BY THIS DOCUMENT. INTEL ASSUMES NO LIABILITY WHATSOEVER AND INTEL DISCLAIMS ANY EXPRESS OR IMPLIED WARRANTY, RELATING TO THIS INFORMATION INCLUDING LIABILITY OR WARRANTIES RELATING TO FITNESS FOR A PARTICULAR PURPOSE, MERCHANTABILITY, OR INFRINGEMENT OF ANY PATENT, COPYRIGHT OR OTHER INTELLECTUAL PROPERTY RIGHT.
Software and workloads used in performance tests may have been optimized for performance only on Intel microprocessors. Performance tests, such as SYSmark and MobileMark, are measured using specific computer systems, components, software, operations and functions. Any change to any of those factors may cause the results to vary. You should consult other information and performance tests to assist you in fully evaluating your contemplated purchases, including the performance of that product when combined with other products.
Copyright © 2014, Intel Corporation. All rights reserved. Intel, Pentium, Xeon, Xeon Phi, Core, VTune, Cilk, and the Intel logo are trademarks of Intel Corporation in the U.S. and other countries.
Optimization Notice
Intel’s compilers may or may not optimize to the same degree for non-Intel microprocessors for optimizations that are not unique to Intel microprocessors. These optimizations include SSE2, SSE3, and SSSE3 instruction sets and other optimizations. Intel does not guarantee the availability, functionality, or effectiveness of any optimization on microprocessors not manufactured by Intel. Microprocessor-dependent optimizations in this product are intended for use with Intel microprocessors. Certain optimizations not specific to Intel microarchitecture are reserved for Intel microprocessors. Please refer to the applicable product User and Reference Guides for more information regarding the specific instruction sets covered by this notice. Notice revision #20110804

## Slide 3: SFI is an Application Centric Framework
Open-Source,
Open-Development, Vendor Supported
Verbs
SFI
Vender Proprietary and Supported
Mellanox: MXM
IBM: PAMI
Cray: uGNI/DMAPP
Research Labs
Sandia: Portals
OSU: MV2-X
ORNL/UH: UCCS
Join the community: http://lists.openfabrics.org/mailman/listinfo/ofiwg
Get the code: https://github.com/ofiwg/libfabric
Notes: MVAPICH:
Unified runtime for hybrid programming model customized for verbs
Reduced resource consumption-sharing resources
MXM/Scalable SHMEM
co-designed to overcoming scalability issues to improve efficiency
50x improvement over current verbs mapping
Cray uGNI/DMAPP
DMAPP: exposes low level operations suited for SHMEM
uGNI: expose communication capabilities of Gemini router
PAMI
Common messaging interface for IBM HPC platforms
Extensible to verbs
SHMEM/MPI
APGAS runtime
Maximizes parallelism in communication library
UCCS (universal common communication substrate)
RMA and atomics to better support SHMEM model
Universal network abstraction for PGAS and MPI
SHMEM reference implementation, portable but clunky
Vs. UCCS not as clunky?

## Slide 4: SFI Architecture
PGAS 2014

## Slide 5: Tutorial: Explore OpenSHMEM to SFI Mappings
PGAS 2014
Goal: Implement Basic OpenSHMEM Pingpong test (sping.c)
start_pes()
shmem_barrier_all()
shmem_wait()
shmem_long_put()
shmem_barrier_all()
shmem_long_put()
start_pes()
shmem_barrier_all()
shmem_wait()
shmem_barrier_all()
PE 0 (sping)
PE 1 (sping)

## Slide 6: OpenSHMEM to SFI Mapping
Implements
Domains
Endpoints
start_pes()
PGAS 2014
Implements
Tagged
shfree()
shmalloc()
barrier_all()
Implements
RMA
shmem_long_put()
Memory Regions
Implements
shmem_wait()
Counters
Event Queues

## Slide 7: Initialization: shmem.c library stubs
PGAS 2014
#include "shmem_impl.h"
global_t _g;
void start_pes (int npes){
SHMEMI_Start_pes(npes);
}
int _my_pe (void){
return SHMEMI_My_pe();
}
int _num_pes (void){
return SHMEMI_Num_pes();
}
void shfree (void *ptr){
SHMEMI_Shfree(ptr);
}
void *shmalloc (size_t size){
return SHMEMI_Shmalloc(size);
}
void shmem_barrier_all (void){
SHMEMI_Barrier_all();
}
void shmem_long_put (long *dest,
const long *src,
size_t nelems,
int pe){
SHMEMI_Long_put(dest,src,nelems,pe);
}
void shmem_wait (long *ivar,
long cmp_value){
SHMEMI_Wait(ivar,cmp_value);
}
/* Global Object for state tracking */
typedef struct global_t
{
struct fid_fabric *fabric;
struct fid_domain *domain;
struct fid_ep *endpoint;
struct fid_ep *endpoint_tag;
struct fid_cntr *putcntr;
struct fid_cntr *getcntr;
struct fid_cntr *targetcntr;
struct fid_cq *cq;
struct fid_cq *cq_tag;
struct fid_av *av;
struct fid_mr *mr;
char epname[EPNAMELEN];
char kvsname[KVSNAMELEN];
int rank;
int size;
uint64_t put_ctr_pending;
}global_t;

## Slide 8: Initialization: Process Manager
PGAS 2014
void SHMEMI_Start_pes(int npes)
{
int i, spawned,jobid;
size_t epnamelen = sizeof(_g.epname);
struct fi_info *p_info = NULL;
struct fi_info *p_info_tag = NULL;
struct fi_info hints;
struct fi_cq_attr cq_attr;
struct fi_av_attr av_attr;
struct fi_cntr_attr cntr_attr;
struct fi_domain_attr domain_attr;
memset(&hints, 0, sizeof(hints));
memset(&cq_attr, 0, sizeof(cq_attr));
…
/* ************************************* */
/* Initialize job launch runtime */
/* ************************************* */
ERRCHKPMI(PMI_Init(&spawned));
…

## Slide 9: Initialization: Query SFI for RMA
fi_getinfo will be the first call you make to SFI
Filter hardware with RDM (reliable messages) via ep_cap.
Request and filter RMA capability
Request remote completion, and set default via op_flags
Request dynamic memory registration and user provided keys
Get back a list of “provider info” structures
hints.type = FI_EP_RDM; /* reliable connectionless */
hints.ep_cap = FI_RMA; /* request rma capability */
hints.ep_cap |= FI_REMOTE_COMPLETE; /* remote completion */
hints.op_flags = FI_REMOTE_COMPLETE; /* By default: generate completions */
domain_attr.caps = FI_USER_MR_KEY; /* Allow user provided rkey to be set */
domain_attr.caps |= FI_DYNAMIC_MR; /* Allow dynamic registration of any memory */
domain_attr.progess_model = FI_PROGRESS_AUTO; /* Automatic progress */
hints.domain_attr = &domain_attr;
ERRCHKSFI(fi_getinfo(FI_VERSION(1,0), /* Interface version requested */
NULL, /* Optional name or fabric to resolve */
"0", /* Service name or port number to request*/
FI_SOURCE, /* Flag: node/service local address*/
&hints, /* In: Hints to filter available providers*/
&p_info)); /* Out: List of providers that match hints */

## Slide 10: Initialization: What about tagged?
RMA
Vs Tagged
hints.ep_cap = FI_RMA; /* request rma capability */
hints.ep_cap |= FI_REMOTE_COMPLETE; /* remote completion */
hints.op_flags = FI_REMOTE_COMPLETE; /* By default: generate completions */
ERRCHKSFI(fi_getinfo(FI_VERSION(1,0), /* Interface version requested */
NULL, /* Optional name or fabric to resolve */
"0", /* Service name or port number to request */
FI_SOURCE, /* Flag: node/service specify local address */
&hints, /* In: Hints to filter available providers */
&p_info)); /* Out: List of providers that match hints */
hints.ep_cap =FI_TAGGED;
hints.ep_cap |=FI_BUFFERED_RECV;
hints.ep_cap |=FI_REMOTE_COMPLETE;
hints.op_flags = FI_REMOTE_COMPLETE;
ERRCHKSFI(fi_getinfo(FI_VERSION(1,0), /* Interface version requested */
NULL, /* Optional name or fabric to resolve */
"0", /* Service name or port number to request */
FI_SOURCE, /* Flag: node/service specify local address */
&hints, /* In: Hints to filter available providers */
&p_info_tag)); /* Out: List of providers that match hints */

## Slide 11: Initialization: Fabric and Domain
/* **************************************************** */
/* The provider info struct returns a fabric attribute */
/* struct that can be used to instantiate the virtual */
/* or physical network. This opens a "fabric provider" */
/* We choose the first available fabric, but getinfo */
/* returns a list. see man fi_fabric for details */
/* **************************************************** */
ERRCHKSFI(fi_fabric(p_info->fabric_attr, /* In: Fabric attributes */
&_g.fabric, /* Out: Fabric descriptor */
NULL)); /* Context: fabric events */
/* **************************************************** */
/* Create the access domain, which is the physical or */
/* virtual network or hardware port or collection of */
/* ports. Returns a domain object that can be used */
/* to create endpoints. See man fi_domain for details */
/* **************************************************** */
ERRCHKSFI(fi_fdomain(_g.fabric, /* In: Fabric object */
p_info->domain_attr, /* In: default domain attributes */
&_g.domain, /* Out: domain object */
NULL)); /* Context: Domain events */

## Slide 12: Initialization: Create the Endpoints
PGAS 2014
/* **************************************************** */
/* Create a transport level communication endpoint. */
/* To use the endpoint, it must be bound to completion */
/* counters or event queues and enabled, and the */
/* resources consumed by it, such as address vectors, */
/* counters, completion queues, etc */
/* see man fi_endpoint for more details */
/* **************************************************** */
ERRCHKSFI(fi_endpoint(_g.domain, /* In: Domain Object */
p_info, /* In: Configuration object */
&_g.endpoint, /* Out: Endpoint Object */
NULL)); /* Context: endpoint events */
ERRCHKSFI(fi_endpoint(_g.domain, /* In: Domain Object */
p_info_tag, /* In: Configuration object */
&_g.endpoint_tag, /* Out: Endpoint Object */
NULL)); /* Context: endpoint events */

## Slide 13: Initialization: Create Objects: Counters
PGAS 2014
/* **************************************************** */
/* First, create the objects that will be bound to the */
/* endpoint. The objects include: */
/* * completion counters for put and get */
/* * counters for incoming writes */
/* * completion queue for events */
/* * address vector of other endpoint addresses */
/* * memory region for symmetric heap */
/* **************************************************** */
cntr_attr.events = FI_CNTR_EVENTS_COMP;
ERRCHKSFI(fi_cntr_open(_g.domain, /* In: Domain Object */
&cntr_attr, /* In: Configuration object */
&_g.putcntr, /* Out: Counter Object */
NULL)); /* Context: counter events */
…
/* Create get counter and remote update counter */

## Slide 14: Initialization: Create Objects: Completion Queues, Address Vector
PGAS 2014
cq_attr.format = FI_CQ_FORMAT_CONTEXT;
cq_attr.size = 1000;
ERRCHKSFI(fi_cq_open(_g.domain, /* In: Domain Object */
&cq_attr, /* In: Configuration object */
&_g.cq, /* Out: CQ Object */
NULL)); /* Context: CQ events */
cq_attr.format = FI_CQ_FORMAT_TAGGED;
ERRCHKSFI(fi_cq_open(_g.domain, /* In: Domain Object */
&cq_attr, /* In: Configuration object */
&_g.cq_tag, /* Out: CQ Object */
NULL)); /* Context: CQ events */
av_attr.type = FI_AV_TABLE; /* Logical addressing mode */
ERRCHKSFI(fi_av_open(_g.domain, /* In: Domain Object */
&av_attr, /* In: Configuration object */
&_g.av, /* Out: AV Object */
NULL)); /* Context: AV events */

## Slide 15: Initialization: Create Objects: Memory Region
PGAS 2014
Hardware and Provider Dependencies
Simple: register all memory with key 0
Dynamic memory regions may not be allowed
User specified key may not be allowed
Query/Hint your provider for capabilities!
ERRCHKSFI(fi_mr_reg(_g.domain, /* In: Domain Object */
0, /* In: Lower address */
UINT64_MAX, /* In: Upper address */
FI_REMOTE_READ | /* In: Expose MR for read/write */
FI_REMOTE_WRITE,
0, /* In: offset */
0ULL, /* In: requested key */
FI_MR_KEY, /* In: specifies to use key field*/
&_g.mr, /* Out: memregion object */
NULL)); /* Context: memregion events */

## Slide 16: Initialization: Bind to Associate Objects
What is Bind?
Associates and connects objects and resources
Counter to Endpoint
Completion Queue to Endpoint
Counter to Memory Region
Endpoint to Address Vector
Memory Region to Endpoint
/* **************************************************** */
/* Bind the counters and CQ to the endpoint */
/* **************************************************** */
ERRCHKSFI(fi_bind(&_g.endpoint->fid,
&_g.putcntr->fid,
FI_WRITE));
ERRCHKSFI(fi_bind(&_g.endpoint->fid,
&_g.getcntr->fid,
FI_READ));
… /* Other object associations */

## Slide 17: Initialization: Enable the Endpoints and Exchange AV Information
PGAS 2014
AV Exchange via published endpoint names:
Commit bind associations with fi_enable
Exchange address names with scalable database
SFI has connection management apis(outside scope)
/* **************************************************** */
/* Enable the endpoints for communication */
/* **************************************************** */
ERRCHKSFI(fi_enable(_g.endpoint));
ERRCHKSFI(fi_enable(_g.endpoint_tag));
/* **************************************************** */
/* Exchange endpoint addresses using scalable database */
/* or job launcher, in this case, use interfaces */
/* **************************************************** */
ERRCHKSFI(fi_getname((fid_t)_g.endpoint, _g.epname, &epnamelen));
…
/* Use scalable database to exchange names */

## Slide 18: Initialization: Map the Exchanged Address Names
PGAS 2014
Address Registration:
Register address names with SFI
Clean up resources
Initialization is done. It’s easy from here on!
/* **************************************************** */
/* Map the addresses into an address vector */
/* The addressing mode is logical so destinations can */
/* be addressed by index */
/* **************************************************** */
ERRCHKSFI(fi_av_map(_g.av, /* Address vector */
addrNames, /* Array of address names, size of addrlen */
_g.size, /* Count of addresses */
NULL, /* Output addresses, unused in logical */
0)); /* FLAGS: none required */

## Slide 19: Symmetric Heap
PGAS 2014
2 Options for symmetric heap
Fixed allocation + suballocator
Dynamic allocation + Collectives (requires Broadcast, Allreduce, Barrier)
void shfree (void *ptr){
SHMEMI_Shfree(ptr);
}
void *shmalloc (size_t size){
return SHMEMI_Shmalloc(size);
}
void SHMEMI_Shfree(void *ptr)
{
long page_sz = sysconf(_SC_PAGESIZE);
char *back = (char*)ptr - page_sz;
size_t *valptr= (size_t*)back;
size_t val = *valptr;
SHMEMI_barrier();
munmap(back, val);
}
void *SHMEMI_Shmalloc (size_t size)
{
SHMEMI_barrier();
long page_sz = sysconf(_SC_PAGESIZE);
void *m = SHMEMI_Symmetric_heap(size+page_sz);
char *ptr = (char*)m + page_sz;
size_t *val = (size_t*)m;
*val = size;
return (void*)ptr;
}

## Slide 20: Symmetric Heap Allocator
PGAS 2014
On root, generate random address
Broadcast address to all PE’s (algorithm shown)
Allreduce result, repeat if address not obtained
int SHMEMI_bcast(void *buf, size_t len){
request_t req;
if(_g.size == 1) return 0;
if(_g.rank == 0) {
SHMEMI_send(buf, len, 1, &req);
while(!req.done)
SHMEMI_poll();
}
else if(_g.rank == _g.size-1){
SHMEMI_recv(buf, len, _g.rank-1, &req);
while(!req.done)
SHMEMI_poll();
}
else{
SHMEMI_recv(buf, len, _g.rank-1, &req);
while(!req.done)
SHMEMI_poll();
SHMEMI_send(buf, len, _g.rank+1, &req);
while(!req.done)
SHMEMI_poll();
}
return 0;
}

## Slide 21: Collectives
PGAS 2014
void shmem_barrier_all (void){
SHMEMI_Barrier_all();
}
void SHMEMI_Barrier_all (void)
{
SHMEMI_quiet();
SHMEMI_barrier();
}
void SHMEMI_quiet(){
ERRCHKSFI(fi_cntr_wait(_g.putcntr,
_g.put_ctr_pending,
-1));
}
int SHMEMI_barrier(){
int i,n;
int nphases = 0;
request_t req[2];
for (n=_g.size-1;n>0;n>>=1)nphases++;
for (i=0; i<nphases; i++)
{
int shift = (1<<i);
int to = (_g.rank+shift)%_g.size;
int from = (_g.rank)-shift;
if(from<0) from = _g.size+from;
char val;
SHMEMI_recv(&val, 1, from,&req[0]);
SHMEMI_send(&val, 1, to, &req[1]);
while(!req[0].done || !req[1].done)
SHMEMI_poll();
}
return 0;
}
Quiet
Waits for local completion via global counter.
Barrier
Log n exchange
Uses tagged send/recv

## Slide 22: Tagged Point to Point (for Collectives)
PGAS 2014
int SHMEMI_send(void *buf, size_t len, int dest, request_t *req)
{
uint64_t match_bits = _g.rank+1000;
req->cb = SHMEMI_Send_cb;
req->done = 0;
ERRCHKSFI(fi_tsendto(_g.endpoint_tag,buf,len,_g.mr,
dest,match_bits,(void*)&req->context));
return 0;
}
int SHMEMI_recv(void *buf, size_t len, int dest, request_t *req)
{
uint64_t match_bits = dest+1000;
uint64_t ignore_bits = 0;
req->cb = SHMEMI_Recv_cb;
req->done = 0;
ERRCHKSFI(fi_trecvfrom(_g.endpoint_tag,buf,len,_g.mr,dest,
match_bits,ignore_bits,(void*)&req->context));
return 0;
}

## Slide 23: Contexts, Requests and Callbacks
PGAS 2014
/* SFI Callback structure */
typedef int (*callback_fn) (struct request*);
/* Request object for tagged send/recv */
typedef struct request
{
struct fi_context context; /* Nonblocking Handle */
callback_fn cb; /* Callback function */
int done; /* Request state */
}request_t;

## Slide 24: Polling For Completions
PGAS 2014
int SHMEMI_poll()
{
ssize_t ret;
completion_entry_t entry;
request_t *req;
ret = fi_cq_read(_g.cq,(void*)&entry,sizeof(entry));
assert(ret >= 0);
if(ret > 0)
{
req = (request_t*)entry.rma.op_context;
req->cb(req);
}
ret = fi_cq_read(_g.cq_tag,(void*)&entry,sizeof(entry));
assert(ret >= 0);
if(ret > 0)
{
req = (request_t*)entry.tagged.op_context;
req->cb(req);
}
return 0;
}
Poll RMA Endpoint
Poll Tagged Endpoint

## Slide 25: Finally. SHMEM Put
void SHMEMI_Long_put (long *dest,
const long *src,
size_t nelems,
int pe)
{
ERRCHKSFI(fi_writeto(_g.endpoint, /* Endpoint */
src, /* Origin buffer */
nelems*sizeof(long), /* buffer size */
_g.mr, /* Memory region */
pe, /* Destination Address */
(uint64_t)dest, /* Target buffer */
0ULL, /* Key */
NULL));
_g.put_ctr_pending++;
SHMEMI_quiet();
}
Flush pending put
Call fi_writeto
Increment pending counter
Call fi_inject_writeto
Increment pending counter
OR….

## Slide 26: Remote Target Synchronization
void shmem_wait (long *ivar,
long cmp_value){
SHMEMI_Wait(ivar,cmp_value);
}
void SHMEMI_Wait (long *ivar,long cmp_value)
{
uint64_t count;
while (*(ivar) == cmp_value)
{
count = fi_cntr_read(_g.targetcntr);
asm volatile("" ::: "memory");
if (*(ivar) != cmp_value) return;
ERRCHKSFI(fi_cntr_wait(_g.targetcntr,
(count + 1),
-1));
}
}
Waits until ivar != cmp_val
Loop until user condition is satisfied
Read counter and wait until value changes (cntr_wait)

## Slide 27: Notes on Inlining
PGAS 2014
It is possible to completely inline SHMEM into your application, directly to your hardware/provider.
  See man FI_DIRECT for info
  Structure shmem to allow for inlining
In shmem_impl.h
In application(sping.c)
#ifdef FORCE_INLINE_SHMEM
#define start_pes SHMEMI_Start_pes
#define _my_pe SHMEMI_My_pe
#define shfree SHMEMI_Shfree
#define shmalloc SHMEMI_Shmalloc
#define shmem_barrier_all SHMEMI_Barrier_all
#define shmem_long_put SHMEMI_Long_put
#define shmem_wait SHMEMI_Wait
#endif
/*#define FORCE_INLINE_SHMEM*/
#ifdef FORCE_INLINE_SHMEM
#include "shmem_impl.h"
#else
#include "shmem.h"
#endif